## Slide 1
Introduce
Creative Computer Engineering Design
Group 4 SMTM
Maze Runner
Key Functions
Implementation Issues
Solutions
Play
Q & A

## Slide 2
        Introduce
        Introduce our Product
SMTM
Maze Runner

## Slide 3
        Introduce
        What is it?
SMTM
It’s Maze Search Machine

## Slide 4
Key Functions
Maze Scanning
Maze Decoding
Moving
Scan the maze on paper using the light sensor.
Interpret the scanned value using the function defined in NXT to determine the appearance of maze
Draw on escape route by moving it from top to bottom based on the detox value.
Functions

## Slide 5
        Key Functions
        - Maze Scanning
SMTM
How are we going to scanning the paper?!
We use Light sensor and detect the color of the block.

## Slide 6
        Key Functions
        - Maze Decoding
SMTM
How are we going to interpret the scanned value?!
Scanning, Saving value, Interpreting, Moving with Robolab.

## Slide 7
        Key Functions
        - Moving
SMTM
And it moves very stable and better performance
How are we going to move through the x, y axes?!
we find the answer is Gear wheel.

## Slide 8
How to make X,Y axes in LEGO and MINDSTORM block?
Implementation Issues
- Most concerned about in implementing
Hardware
Software
How can we make a code in the maze to find and scan the escape route?

## Slide 9
        Solutions
        - Hardware
SMTM
First, We organized the x and y coordinates
X Block
Y Block
It moves vertically
It moves horizontally
But the problem has come.

## Slide 10
        Solutions
        - Hardware
SMTM
The Problem was..
The separation between the blocks and the convex part on the block made the gears unstable.

## Slide 11
        Solutions
        - Hardware
SMTM
The Solution was ?!
Adding another
y-axis motor could make it move
stably

## Slide 12
        Solutions
        - Software
SMTM
How we represent the maze?
wall
route
We scan the all value one by one and use container function in RoboLab
However, the maximum number of containers is limited to 20.

## Slide 13
        Solutions
        - Software
SMTM
The Solution was ?!
Add all the black color in the row to the container by binary digits.
By returning the converted number back to the decimal number, it can then be used as a small container.

## Slide 14
        Solutions
        - Software
SMTM
Algorithm Example
Container has value=
1+0+4+8+16+32+64+128+256+512 = 1021
And decoding time it Determine the mystery shape by rotating the converted decimal value back into binary.

## Slide 15
        Play
        - Demo
SMTM

## Slide 16
        Q&A
        ASK ME!
SMTM

## Slide 17
Thank You
It’s Group 4
S M T M